## Slide 1: Fast Fourier Transform (FFT)
Advantages, Methods, and Examples

## Slide 2: Advantages of FFT
Reduces computational complexity: O(N log N) vs. O(N²) for DFT
Efficient for real-time applications and embedded systems
Reduces memory usage with optimized computations
Essential in audio, image, telecom, and BCI domains
Enables quick spectral/frequency analysis

## Slide 3: FFT Methods
Radix-2 FFT (most common) - for N = power of 2
Radix-4, Radix-8, Mixed-Radix FFT - for composite N
Prime Factor Algorithm (PFA) - for prime-length N
Bluestein’s FFT (Chirp-Z) - converts DFT to convolution

## Slide 4: Example
An 8-point sequence is given by x(n) = {2, 2, 2, 2, 1, 1, 1, 1}.
Compute the 8-point DFT of x(n) by
(a) Radix-2 DIT FFT algorithm

## Slide 5: Example: 8-Point DIT FFT Summary
Step | Action
1 | Input: x[n]
2 | Reorder using bit-reversal
3 | Stage 1: Compute 2-point butterflies
4 | Stage 2: Compute 4-point butterflies
5 | Stage 3: Compute 8-point butterflies
6 | Output: X[k] for k=0 to 7

## Slide 6
(a) Radix-2 DIT FFT algorithm
Radix-2 DIT FFT algorithm

## Slide 7: Example
An 8-point sequence is given by x(n) = {2, 2, 2, 2, 1, 1, 1, 1}.
Compute the 8-point DFT of x(n) by
(b) Radix-2 DIF FFT algorithm

## Slide 8: 8-Point DIF FFT Summary
Step | Action
1 | Input: x[n]={x0​,x1​,...,x7​}
2 | Stage 1: 8-point butterfly groups
3 | Stage 2: 4-point butterfly groups
4 | Stage 3: 2-point butterfly groups
5 | Bit-reverse the output
6 | Result: X[k] frequency domain

## Slide 9: Radix-2 DIF FFT algorithm

## Slide 10: Applications of FFT
Audio: MP3 compression, spectral analysis, EQ
Image: JPEG compression, filtering
Telecom: OFDM, channel estimation
BCI: EEG signal frequency analysis
Engineering: Vibration/fault analysis, radar/sonar

## Slide 11: Summary: DFT vs FFT
DFT complexity: O(N²), FFT: O(N log N)
FFT is practical for large N, DFT is not
FFT enables efficient implementation of frequency-domain analysis