## Slide 1: Digital Signal Processing
Dr. Ravichander Janapati
Professor
Dept. of Electronics & communication Engineering
SR University, Warangal.
Topic: Multi rate Signal Processing

## Slide 2
What does multirate mean?
Multirate simply means “multiple sampling rates”.
A multirate DSP system uses multiple sampling rates within the system.
Whenever a signal at one rate has to be used by a system that expects a different rate, the rate has to be increased or decreased, and some processing is required to do so.
Therefore “Multirate DSP” really refers to the art or science of changing sampling rates.
The process of converting a signal from a given rate to a different rate is called sampling rate conversion.
System that employ multiple sampling rates in the processing of digital signals are called multirate digital signal processing systems.

## Slide 3
Why should I do multirate DSP?
The most immediate reason is when you need to pass data between two systems which use incompatible sampling rates.
For example,
Professional audio systems use 48 kHz rate, but consumer CD players use 44.1 kHz , for broadcasting 32 KHz; when audio professionals transfer their recorded music to CDs, they need to do a rate conversion.
But the most common reason is that multirate DSP can greatly increase processing efficiency which reduces DSP system cost.
Examples of multirate DSP
Signal Compression ,Image coding , Speech coding, A/D and D/A Converter , Communication Systems

## Slide 4
Computational requirements are less
Storage for filter coefficents are less
Finite arithmetic effects are less
Filter order required in multirate application are low
Sensitivity to filter coefficient lengths are less
Various advantages of Multirate DSP
While designing multirate systems, effect of aliasing for decimation and pseudoimages for interpolation should be avoided.

## Slide 5
What are the categories of multirate?
Multirate consists of:
Decimation: To decrease the sampling rate.
2) Interpolation: To increase the sampling rate.
3) Resampling:To combine decimation and interpolation in
order to change the sampling rate by a fractional
value that can be expressed as a ratio.
For example, to resample by a factor of 1.5, just interpolate by a factor of 3 then decimate by a factor of 2 (to change the sampling rate by a factor of 3/2=1.5.)

## Slide 6: Multirate Digital Signal Processing
Basic Sampling Rate Alteration Devices
Up-sampler - Used to increase the sampling
rate by an integer factor
Down-sampler - Used to decrease the sampling
rate by an integer factor

## Slide 7: Up-Sampler
Time-Domain Characterization
An up-sampler with an up-sampling factor L, where L is a positive integer, develops an output sequence with a sampling rate that is L times larger than that of the input sequence x[n] , digital anti-aliasing filter h1(k)
Block-diagram representation
L
x[n]
h1(k)

## Slide 8: Up-Sampler
Up-sampling operation is implemented by inserting equidistant zero-valued samples between two consecutive samples of x[n]
Input-output relation

## Slide 9: Up-Sampler
Figure below shows the up-sampling by a factor of 3 of a sinusoidal sequence with a frequency of 0.12 Hz obtained.

## Slide 10: Up-Sampler
In practice, the zero-valued samples inserted by the up-sampler are replaced with appropriate nonzero values using some type of filtering process
Process is called interpolation and will be discussed later

## Slide 11: Down-Sampler
Time-Domain Characterization
An down-sampler with a down-sampling factor M, where M is a positive integer, develops an output sequence y[n] with a sampling rate that is (1/M)-th of that of the input sequence x[n]
Block-diagram representation
M
x[n]
y[n]

## Slide 12: Down-Sampler
Down-sampling operation is implemented by keeping every M-th sample of x[n] and removing in-between samples to generate y[n]
Input-output relation
y[n] = x[nM]

## Slide 13: Down-Sampler
Figure below shows the down-sampling by a factor of 3 of a sinusoidal sequence of frequency 0.042 Hz.

## Slide 14
X(n)={1,2,3,4}
X(2n)={1,3}----Down sampling
X(n/2)={1,0,2,0,3,0,4,0}---Upsampling
Copyright © 2001, S. K. Mitra

## Slide 15: Basic Sampling Rate Alteration Devices
Sampling periods have not been explicitly shown in the block-diagram representations of the up-sampler and the down-sampler
This is for simplicity and the fact that the mathematical theory of multirate systems can be understood without bringing the sampling period T or the sampling frequency into the picture

## Slide 16: Down-Sampler
Figure below shows explicitly the time-dimensions for the down-sampler
M
Input sampling frequency
Output sampling frequency

## Slide 17: Up-Sampler
Figure below shows explicitly the time-dimensions for the up-sampler
Input sampling frequency
L
y[n]
Output sampling frequency

## Slide 18: Basic Sampling Rate Alteration Devices
The up-sampler and the down-sampler are linear but time-varying discrete-time systems
We illustrate the time-varying property of a down-sampler
The time-varying property of an up-sampler can be proved in a similar manner

## Slide 19: Basic Sampling Rate Alteration Devices
Consider a factor-of-M down-sampler defined by
Its output for an input is then given by
From the input-output relation of the down-sampler we obtain
y[n] = x[nM]

## Slide 20: Up-Sampler
Frequency-Domain Characterization
Consider first a factor-of-2 up-sampler whose input-output relation in the time-domain is given by

## Slide 21: Spectrum of the Up-Sampler
In terms of the z-transform, the input-output relation is then given by

## Slide 22: Cont…
In a similar manner, we can show that for a factor-of-L up-sampler
On the unit circle, for , the input-output relation is given by

## Slide 23: Cont…
Figure below shows the relation between and for L = 2 in the case of a typical sequence x[n]

## Slide 24: Up-Sampler
As can be seen, a factor-of-2 sampling rate expansion leads to a compression of by a factor of 2 and a 2-fold repetition in the baseband [0, 2]
This process is called imaging as we get an additional “image” of the input spectrum

## Slide 25: Up-Sampler
Similarly in the case of a factor-of-L sampling rate expansion, there will be additional images of the input spectrum in the baseband
Lowpass filtering of removes the images and in effect “fills in” the zero-valued samples in with interpolated sample values

## Slide 26: Up-Sampler
Illustrate the frequency-domain properties of the up-sampler shown below for L = 4

## Slide 27: Spectrum of the Down-Sampler
Frequency-Domain Characterization
Applying the z-transform to the input-output relation of a factor-of-M down-sampler
we get
The expression on the right-hand side cannot be directly expressed in terms of X(z)

## Slide 28: Cont…
To get around this problem, define a new sequence :
Then

## Slide 29: Cont…
Now, can be formally related to x[n] through
where
A convenient representation of c[n] is given by
where

## Slide 30: Cont…
Taking the z-transform of and making use of
we arrive at

## Slide 31: Spectrum of the Down-Sampler
Consider a factor-of-2 down-sampler with an input x[n] whose spectrum is as shown below
The DTFTs of the output and the input sequences of this down-sampler are then related as

## Slide 32: Aliasing Effect in Down-Sampler
Now implying that the second term in the previous equation is simply obtained by shifting the first term to the right by an amount 2 as shown below

## Slide 33: Cont…
The plots of the two terms have an overlap, and hence, in general, the original “shape” of is lost when x[n] is down-sampled as indicated below
M
x[n]
y[n]
h(n)

## Slide 34: Cont…
This overlap causes the aliasing that takes place due to under-sampling
There is no overlap, i.e., no aliasing, only if
Note: is indeed periodic with a period 2, even though the stretched version of is periodic with a period 4

## Slide 35: Down-Sampler
For the general case, the relation between the DTFTs of the output and the input of a factor-of-M down-sampler is given by
is a sum of M uniformly shifted and stretched versions of and scaled by a factor of 1/M

## Slide 36: Original and Downsampled Spectrum
Aliasing is absent if and only if
as shown below for M = 2

## Slide 37: Down-Sampler
Illustrate the frequency-domain properties of the up-sampler shown below for M = 2

## Slide 38: Down-Sampler
The input and output spectra of a down-sampler with M = 3 are shown below
Effect of aliasing can be clearly seen

## Slide 39: Cascade Equivalences
A complex multirate system is formed by an interconnection of the up-sampler, the down-sampler, and the components of an LTI digital filter
In many applications these devices appear in a cascade form
An interchange of the positions of the branches in a cascade often can lead to a computationally efficient realization
Fractional Sampling Rate Alteration

## Slide 40: Cascade Equivalences
To implement a fractional change in the sampling rate we need to employ a cascade of an up-sampler and a down-sampler
Consider the two cascade connections shown below
M
L
M
L

## Slide 41: Cascade Equivalences
A cascade of a factor-of-M down-sampler and a factor-of-L up-sampler is interchangeable with no change in the input-output relation:
if and only if M and L are relatively prime, i.e., M and L do not have any common factor that is an integer k > 1

## Slide 42: Cascade Equivalences
Two other cascade equivalences are shown below
L
L
M
M
Cascade equivalence #1
Cascade equivalence #2

## Slide 43: Filters in Sampling Rate Alteration Systems
From the sampling theorem it is known that a the sampling rate of a critically sampled discrete-time signal with a spectrum occupying the full Nyquist range cannot be reduced any further since such a reduction will introduce aliasing
Hence, the bandwidth of a critically sampled signal must be reduced by lowpass filtering before its sampling rate is reduced by a down-sampler

## Slide 44: Signal Flow Graph
A collection of nodes and directed edges
  Node: computation or task
  Directed edge (j,k)
    a linear transformation from node j to node k
    Usually as constant gain multiplier or delay elements
  Widely used in digital filter structures
Basic blocks :

## Slide 45: Block Diagram

## Slide 48: Filters in Sampling Rate Alteration Systems
Likewise, the zero-valued samples introduced by an up-sampler must be interpolated to more appropriate values for an effective sampling rate increase
We shall show next that this interpolation can be achieved simply by digital lowpass filtering
We now develop the frequency response specifications of these lowpass filters

## Slide 49: Filter Specifications
Since up-sampling causes periodic repetition of the basic spectrum, the unwanted images in the spectra of the up-sampled signal must be removed by using a lowpass filter H(z), called the interpolation filter, as indicated below
The above system is called an interpolator
L

## Slide 50: Filter Specifications
Overall filter requirement for decimation, to avoid aliasing after rate reduction are
Passband
Stopband
Passband deviation
Stopband deviation
Where
Fs is the original sampling frequency

## Slide 51: Filter Specifications
Overall filter requirement for interpolation, to avoid aliasing after rate reduction are
Passband
Stopband
Passband deviation
Stopband deviation
Where

## Slide 52: Filter Specifications
On the other hand, prior to down-sampling, the signal v[n] should be bandlimited to by means of a lowpass filter, called the decimation filter, as indicated below to avoid aliasing caused by down-sampling
The above system is called a decimator
M

## Slide 53: Interpolation Filter Specifications
Assume x[n] has been obtained by sampling a continuous-time signal at the Nyquist rate
If and denote the Fourier transforms of and x[n], respectively, then it can be shown
where is the sampling period

## Slide 54: Interpolation Filter Specifications
Since the sampling is being performed at the Nyquist rate, there is no overlap between the shifted spectras of
If we instead sample at a much higher rate yielding y[n], its Fourier transform is related to through

## Slide 55: Interpolation Filter Specifications
On the other hand, if we pass x[n] through a factor-of-L up-sampler generating , the relation between the Fourier transforms of x[n] and are given by
It therefore follows that if is passed through an ideal lowpass filter H(z) with a cutoff at /L and a gain of L, the output of the filter will be precisely y[n]

## Slide 56: Interpolation Filter Specifications
In practice, a transition band is provided to ensure the realizability and stability of the lowpass interpolation filter H(z)
Hence, the desired lowpass filter should have a stopband edge at and a passband edge close to to reduce the distortion of the spectrum of x[n]

## Slide 57: Interpolation Filter Specifications
If is the highest frequency that needs to be preserved in x[n], then
Summarizing the specifications of the lowpass interpolation filter are thus given by

## Slide 58: Decimation Filter Specifications
In a similar manner, we can develop the specifications for the lowpass decimation filter that are given by

## Slide 59: Filter Design Methods
The design of the filter H(z) is a standard IIR or FIR lowpass filter design problem
Any one of the techniques outlined in Chapter 7 can be applied for the design of these lowpass filters

## Slide 60: Filters for Fractional Sampling Rate Alteration
A fractional change in the sampling rate can be achieved by cascading a factor-of-M decimator with a factor-of-L interpolator, where M and L are positive integers
Such a cascade is equivalent to a decimator with a decimation factor of M/L or an interpolator with an interpolation factor of L/M

## Slide 61: Filters for Fractional Sampling Rate Alteration
There are two possible such cascade connections as indicated below
The second scheme is more computationally efficient since only one of the filters, or , is adequate to serve as both the interpolation and the decimation filter
L
M
L
M

## Slide 62: Filters for Fractional Sampling Rate Alteration
Hence, the desired configuration for the fractional sampling rate alteration is as indicated below where the lowpass filter H(z) has a stopband edge frequency given by
L
M

## Slide 63: Computational Requirements
The lowpass decimation or interpolation filter can be designed either as an FIR or an IIR digital filter
In the case of single-rate digital signal processing, IIR digital filters are, in general, computationally more efficient than equivalent FIR digital filters, and are therefore preferred where computational cost needs to be minimized

## Slide 64: Computational Requirements
This issue is not quite the same in the case of multirate digital signal processing
To illustrate this point further, consider the factor-of-M decimator shown below
If the decimation filter H(z) is an FIR filter of length N implemented in a direct form, then
M

## Slide 65: Computational Requirements
Now, the down-sampler keeps only every M-th sample of v[n] at its output
Hence, it is sufficient to compute v[n] only for values of n that are multiples of M and skip the computations of in-between samples
This leads to a factor of M savings in the computational complexity

## Slide 66: Computational Requirements
Now assume H(z) to be an IIR filter of order K with a transfer function
where

## Slide 67: Computational Requirements
Its direct form implementation is given by
Since v[n] is being down-sampled, it is sufficient to compute v[n] only for values of n that are integer multiples of M

## Slide 68: Computational Requirements
However, the intermediate signal w[n] must be computed for all values of n
For example, in the computation of
K+1 successive values of w[n] are still required
As a result, the savings in the computation in this case is going to be less than a factor of M

## Slide 69: Computational Requirements
For the case of interpolator design, very similar arguments hold
If H(z) is an FIR interpolation filter, then the computational savings is by a factor of L (since v[n] has zeros between its consecutive nonzero samples)
On the other hand, computational savings is significantly less with IIR filters

## Slide 70: Filter Bank
For multirate processing it is required to separate
a signal into a set of sub- bands signals.
In some application where these kind of sub-band have to be combined .
For this Filter Banks are used.
  Analysis Filter Bank
  Synthesis Filter Bank
  Sub-Band Coding Filter Bank
  Quadrature-Mirror Filter Bank

## Slide 71: 1) Analysis Filter Bank
It consist of M-sub filter.
The individual Hk(z) is known as analysis filter.
All the sub filter are equally spaced in frequancy
and each have the same frequancy.

## Slide 72: 2) Synthesis Filter Bank
It is dual of M-channel analysis bank K.
Each Um(z) is fed to upsampler.
The upsampling process produced the signal Um(zm)

## Slide 73: 3) Sub-Band Coding Filter Bank
It is obtained by combining analysis and synthesis filter bank.
Analysis filter bank splits the broadband input signal x(n).
Synthesis filter bank is used to reconstruct output signal x(n)

## Slide 74: 4) Quadrature Mirror Filter Bank
It is a two channel sub-band coding filter bank with complementary frequency response.
It consist of two sections
1) Analysis section ,
Ho(z) –lowpass filter , H1(z) –highpass filter
2) Synthesis Section
Go(z) –lowpass filter , G1(z) –highpass filter

## Slide 75: Application of Multirate DSP
High Quality Analog to Digital Conversion for Digital Audio.
Efficient Digital to Analog Conversion in Compact Hi-Fi Systems.
Applicationin the Acquisition of High Quality Data.
Multirate Narrowband Filtering.
(Sharp transition between passband and stopbands)

## Slide 76: DSP Processor TMS320C54x

## Slide 77: Texas Instruments TMS320 Family Multiple DSP P Generations

## Slide 78: Features of TMS320C54x
Features provided by the ’54x DSPs include:
High-performance, low-power ’C54x CPU
Advanced multibus architecture with three separate 16-bit data memory buses and one program memory bus
40-bit arithmetic logic unit (ALU), including a 40-bit barrel shifter and two independent 40-bit accumulators
17- × 17-bit parallel multiplier coupled to a 40-bit dedicated adder for nonpipelined single-cycle multiply/accumulate (MAC) operation
Compare, select, and store unit (CSSU) for the add/compare
selection of the Viterbi operator
Exponent encoder to compute an exponent value of a 40-bit
accumulator value in a single cycle

## Slide 79: Cont…
Two address generators with eight auxiliary registers and two
auxiliary register arithmetic units (ARAUs)
Data buses with a bus holder feature
Extended addressing mode for up to 8M × 16-bit maximum
addressable external program space
Single-instruction repeat and block-repeat operations for program
Code
Block-memory-move instructions for better program and data
management
Instructions with a 32-bit-long word operand
Instructions with two- or three-operand reads
Arithmetic instructions with parallel store and parallel load
Conditional store instructions
Fast return from interrupt

## Slide 80: On-chip peripherals :
Software-programmable wait-state generator and programmable bank-switching
Phase-locked loop (PLL) clock generator with internal crystal
oscillator or external clock source
Full-duplex standard serial port
Time-division multiplexed (TDM) serial port
Buffered serial port (BSP)
Multichannel buffered serial port (McBSP)
Direct memory access (DMA) controller
8-bit parallel host-port interface (HPI)
Enhanced 8-bit parallel host-port interface (HPI8)
16-bit parallel host-port interface (HPI16)
16-bit timer with 4-bit prescaler
Interprocessor first-in first-out (FIFO) unit (on multiple CPU
devices)

## Slide 81
Architecture
The ’54x DSPs use an advanced, modified Harvard architecture that maximizes processing power by maintaining one program memory bus and three data memory buses. These processors also provide an arithmetic logic unit (ALU) that has a high degree of parallelism, application-specific hardware logic, on-chip memory, and additional on-chip peripherals. These DSP families also provide a highly specialized instruction set, which is the basis of the operational flexibility and speed of these DSPs.

## Slide 82: Cont….
Separate program and data spaces allow simultaneous access to program instructions and data, providing the high degree of parallelism. Two reads and one write operation can be performed in a single cycle. Instructions with parallel store and application-specific instructions can fully utilize this architecture. In addition, data can be transferred between data and program spaces. Such parallelism supports a powerful set of arithmetic, logic, and bit-manipulation operations that can all be performed in a single machine cycle. Also included are the control mechanisms to manage interrupts, repeated operations, and function calls.

## Slide 83: TMS320C54x Internal Block Diagram

## Slide 84
Central Processing Unit (CPU)
  The CPU of the ’54x devices contains:
  A 40-bit arithmetic logic unit (ALU)
  Two 40-bit accumulators
  A barrel shifter
  A 17 × 17-bit multiplier/adder
  A compare, select, and store unit (CSSU)
Arithmetic Logic Unit (ALU)
  The ’54x devices perform 2s-complement arithmetic using a 40-bit ALU and two 40-bit accumulators (ACCA and ACCB). The ALU also can perform Boolean operations.
  The ALU can function as two 16-bit ALUs and perform two 16-bit operations simultaneously when the C16 bit in status register 1 (ST1) is set.

## Slide 85
Accumulators
The accumulators, ACCA and ACCB, store the output from the ALU or the multiplier / adder block; the accumulators can also provide a second input to the ALU or the multiplier / adder. The bits in each accumulator is grouped as follows:
Guard bits (bits 32–39)
A high-order word (bits 16–31)
A low-order word (bits 0–15)
Instructions are provided for storing the guard bits, the high-order and the low-order accumulator words in data memory, and for manipulating 32-bit accumulator words in or out of data memory. Also, any of the accumulators can be used as temporary storage for the other.

## Slide 86
Barrel Shifter
The ’54x’s barrel shifter has a 40-bit input connected to the accumulator or data memory (CB, DB) and a 40-bit output connected to the ALU or data memory (EB). The barrel shifter produces a left shift of 0 to 31 bits and a right shift of 0 to 16 bits on the input data.
Multiplier/Adder
The multiplier / adder performs 17 × 17-bit 2s-complement multiplication with a 40-bit accumulation in a single instruction cycle. The multiplier / adder block consists of several elements: a multiplier, adder, signed/unsigned input control, fractional control, a zero detector, a rounder (2s-complement), overflow/saturation logic, and TREG. The multiplier has two inputs: one input is selected from the TREG, a data-memory operand, or an accumulator; the other is selected from the program memory, the data memory, an accumulator, or an immediate value. The fast on-chip multiplier allows the ’54x to perform operations such as convolution, correlation, and filtering efficiently.

## Slide 87
Compare, Select, and Store Unit (CSSU)
The compare, select, and store unit (CSSU) performs maximum comparisons between the accumulator’s high and low words, allows the test/control (TC) flag bit of status register 0 (ST0) and the transition (TRN) register to keep their transition histories, and selects the larger word in the accumulator to be stored in data memory. The CSSU also accelerates Viterbi-type butterfly computation with optimized on-chip hardware.
Program Control
Program control is provided by several hardware and software mechanisms:
Some of the hardware elements included in the program controller are the program counter, the status and control register, the stack, and the address-generation logic.
Some of the software mechanisms used for program control include branches, calls, conditional instructions, a repeat instruction, reset, and interrupts.

## Slide 88
Status Registers (ST0, ST1)
The status registers, ST0 and ST1, contain the status of the various conditions and modes for the ’54x devices. ST0 contains the flags (OV, C, and TC) produced by arithmetic operations and bit manipulations in addition to the data page pointer (DP) and the auxiliary register pointer (ARP) fields. ST1 contains the various modes and instructions that the processor operates on and executes.
Auxiliary Registers (AR0–AR7)
The eight 16-bit auxiliary registers (AR0–AR7) can be accessed by the central airthmetic logic unit (CALU) and modified by the auxiliary register arithmetic units (ARAUs). The primary function of the auxiliary registers is generating 16-bit addresses for data space. However, these registers also can act as general-purpose registers or counters.

## Slide 89
Temporary Register (TREG)
The TREG is used to hold one of the multiplicands for multiply and multiply/accumulate instructions. It can hold a dynamic (execution-time programmable) shift count for instructions with a shift operation such as ADD, LD, and SUB. It also can hold a dynamic bit address for the BITT instruction.
Transition Register (TRN)
The TRN is a 16-bit register that is used to hold the transition decision for the path to new metrics to perform the Viterbi algorithm. The CMPS (compare, select, max, and store) instruction updates the contents of the TRN based on the comparison between the accumulator high word and the accumulator low word.

## Slide 90
Stack-Pointer Register (SP)
The SP is a 16-bit register that contains the address at the top of the system stack. The SP always points to the last element pushed onto the stack. The stack is manipulated by interrupts, traps, calls, returns, and the PUSHD, PSHM, POPD, and POPM instructions. Pushes and pops of the stack predecrement and postincrement, respectively, all 16 bits of the SP.
Circular-Buffer-Size Register (BK)
The 16-bit BK is used by the ARAUs in circular addressing to specify the data block size.

## Slide 91
Block-Repeat Registers (BRC, RSA, REA)
The block-repeat counter (BRC) is a 16-bit register used to specify the number of times a block of code is to be repeated when performing a block repeat. The block-repeat start address (RSA) is a 16-bit register containing the starting address of the block of program memory to be repeated when operating in the
repeat mode. The 16-bit block-repeat end address (REA) contains the ending address if the block of program memory is to be repeated when operating in the repeat mode.
Interrupt Registers (IMR, IFR)
The interrupt-mask register (IMR) is used to mask off specific interrupts individually at required times. The interrupt-flag register (IFR) indicates the current status of the interrupts.

## Slide 92
Processor-Mode Status Register (PMST)
The processor-mode status register (PMST) controls memory configurations of the ’54x devices.
Power-Down Modes
There are three power-down modes, activated by the IDLE1, IDLE2, and IDLE3 instructions. In these modes, the ’54x devices enter a dormant state and dissipate considerably less power than in normal operation.
The IDLE1 instruction is used to shut down the CPU.
The IDLE2 instruction is used to shut down the CPU and on-chip peripherals.
The IDLE3 instruction is used to shut down the ’54x processor completely. This instruction stops the PLL circuitry as well as the CPU and peripherals.

## Slide 93: Thank You